## Name ______________________________________

## Before you begin, save this Lab Report Template on your computer as LastNameAPChem13a

## Title: Enthalpy of Fusion of Ice

Purpose:

To measure temperature changes as ice melts in water

To calculate heat changes from experimental data

To calculate the

Materials:

| hot tap water ice chips balance or calibrated foam cup thermometer | foam coffee cup metric ruler plastic cup marker |
| --- | --- |

Procedure:

If a balance is not available, use the Calorimeter Calibration Method below

- Add 25.0  mL hot water to foam cup and record mass and temperature

- Add a few ice chips to the water in the cup, stir, record mass, volume, and temperature AFTER the ice has completely melted.

- Record your data in Data Table 1, below
(Convert volume to mass if a balance is not available)

- Calculate the enthalpy of fusion of ice, using the steps in Data Table 2 below.

- Repeat procedure several times, using 10 ml, 30 mL, 40 mL, and 50 mL water.

- You should repeat the experiments until you have consistent data

| Calorimeter Calibration Method Add 5.00 mL tap water to cup and mark level Add water at 5.00 mL increments, marking the level each time Convert mL levels to grams, using the temperature-density data for tap water ( Sample Calculation at 40oC 25 mL H2O x 0.992 g/mL = 24.8 g H2O | Temperature (oC) | Density of Tap Water (g/mL) |
| --- | --- | --- |
|  | 0 | 0.999 |
|  | 4 | 0.999 |
|  | 10 | 0.999 |
|  | 20 | 0.998 |
|  | 30 | 0.995 |
|  | 40 | 0.992 |
|  | 50 | 0.989 |
|  | 60 | 0.984 |
|  | 60 | 0.980 |
|  | 80 | 0.975 |
|  | 90 | 0.965 |
|  | 100 | Steam! |

Results:

| Data Table 1: Experimental Data |
| --- |
| Trial ( | 1 | 2 | 3 | 4 | 5 |
| initial volume of hot water (mL) |  |  |  |  |  |
| mass of hot water (g) |  |  |  |  |  |
| initial temperature of water (oC) |  |  |  |  |  |
| final temperature (water + melted ice) (oC) |  |  |  |  |  |
| final volume (water + melted ice) (mL) |  |  |  |  |  |
| total mass (water + melted ice) |  |  |  |  |  |
| ice temperature (oC) | 0 | 0 | 0 | 0 | 0 |
| Data Table 2: Calculations |
| Quantity | Calculation |  |  |  |  |  |
| mass of ice | d − a |  |  |  |  |  |
| ΔT for hot water (oC) (Tf − Ti) | c − b |  |  |  |  |  |
| heat lost by water (cal) | a x (c − b) x 1 |  |  |  |  |  |
| ΔT for ice (oC) | c − e |  |  |  |  |  |
| heat gained by ice (oC) | f x (c − e) x 1 |  |  |  |  |  |
| heat lost + heat gained (cal) | h + j |  |  |  |  |  |
| heat of fusion of ice (cal/g) | -k/f |  |  |  |  |  |
| percent error A = 80 cal/g or |  |  |  |  |  |  |
| heat of fusion of ice (J/g) | use 4.18 J = 1 cal |  |  |  |  |  |
| percent error A = 334 J/g |  |  |  |  |  |  |
| molar heat of fusion (kJ/mol) | n x 18.0 g/mol x 1 kg/103 J |  |  |  |  |  |
| percent error A = 6.05 kJ/mol |  |  |  |  |  |  |

Analysis Questions

- Explain why ΔT for the hot water is negative. What does the negative sign indicate in terms of energy flow?

- In your calculations, you assumed that the temperature of ice is 0 oC. Explain this assumption.

- Is the sign of the heat absorbed by the ice positive or negative? Explain.

- Were your percent error values lower or higher when you started out with a larger sample of water? Explain.

- Indicate sources of error

Conclusion:  State the following values

- average heat of fusion of ice ± percent error in cal/g

- average heat of fusion of ice ± percent error in J/g

- average molar heat of fusion in ± percent error in kJ/mol

Reflection: Personal commentary about what you learned from the lab activity